## Slide 1
Relay switching
Proton precession magnetometer, ECE 455
Relay design research and LTspice contact-transfer simulations
Fall 2026
Notes: Scope: DPDT relay routing and relay contact-transfer simulation only. Amplifier and filter design belongs to another team. This deck does not cover the polarization power circuit or the Arduino receive interface.

## Slide 2
DPDT relay contact schematic
02
The two common contacts stay connected to the sensor coil. K1 selects polarization or receive on both leads.
POLARIZATION
RECEIVE INPUT
K1 · DPDT relay
SENSOR COIL
POL_A
RX_A
K1A
COM1
COIL_A
POL_B
RX_B
K1B
COM2
COIL_B
K1 coil
RELAY_EN
Released: COM–NC. Energized: COM–NO (dashed blade).
Coil-driver circuitry is outside this contact-only simulation.
Notes: Schematic of the relay contact routing in the relay-only scope. K1 is shown released, so COM1/2 connect to NC1/2 (the receive inputs). When energized, both blades move to NO1/2 and connect the sensor coil leads to POL_A/POL_B. The pale dashed blades show the energized alternative. The relay coil is controlled by RELAY_EN; its transistor driver, coil supply, flyback protection, and mechanical behavior are not part of the contact-transfer simulation. Contact routing is grounded in PyPPM v1.3 relay schematic Sheet 13 and in the project relay architecture described in DESIGN.md under “Magnetometer reference projects”. PyPPM source: https://github.com/geekysuavo/pyppm/blob/main/designs/ppm-1.3/13-relay.sch

## Slide 3
Relay research informed the switching architecture
03
PyPPM v1.3
Relay schematic · Sheet 13
Reference for the two-pole relay arrangement between polarization and receive paths.
Sri Lanka build · 2008
Construction of a Proton Magnetometer
Reference for sequencing the coil between polarization and measurement.
JPM-4 · 2021
Relay-controlled measurement cycle
Reference for switching from polarization to receive and coordinating the measurement cycle.
These references ground the contact-routing concept. The LTspice contact model does not establish a selected relay’s mechanical timing or bounce.
Notes: References used for the relay-only scope:
[1] PyPPM v1.3, relay schematic Sheet 13: https://github.com/geekysuavo/pyppm/blob/main/designs/ppm-1.3/13-relay.sch
[2] W. D. S. Ruhunusiri and M. K. Jayananda, “Construction of a Proton Magnetometer” (2008): https://ipsl.lk/documents/TechSession/2008/ipsl0812.pdf
[3] X. Gong et al., “JPM-4 Proton Precession Magnetometer and Sensitivity Estimation” (2021): https://sensors.myu-group.co.jp/sm_pdf/SM2789.pdf
Project source: DESIGN.md, “Magnetometer reference projects”; MEASURING_CIRCUIT_AND_RELAY.md.

## Slide 4
LTspice relay contact model
04
Four voltage-controlled switches represent the two NO and two NC contacts. A single command moves both poles.
Energizing
As RELAY_EN rises, the NC path opens at 2.2 V. The NO path closes at 3.2 V.
Modeled all-open interval: 2.2–3.2 V.
Releasing
As RELAY_EN falls, the NO path opens at 2.8 V. The NC path closes at 1.8 V.
Modeled all-open interval: 1.8–2.8 V.
The simulation tests contact routing and break-before-make logic. It does not model the relay coil, driver MOSFET, mechanical delay, or contact bounce.
Notes: The relay contact model is adapted from the relay section of LTSpice/complete_system/complete_system.cir. SW_NO uses Ron=20 mΩ, Roff=100 MΩ, Von=3.2 V, Voff=2.8 V. SW_NC is controlled by the inverted relay command and uses Von=-1.8 V, Voff=-2.2 V; therefore the NC contact opens at relay command 2.2 V on the rising edge and closes below 1.8 V on the falling edge. This is a logical switch model, not a model of relay coil pull-in/drop-out or mechanical contact bounce.

## Slide 5
LTspice relay contact simulations
05
Relay-only 16 ms transient · ideal contact switches · test voltages distinguish the two paths
Chart: Relay command
Chart: Both coil-lead routes
Chart: Energizing transition
The command rises from 0 to 5 V at 1.0–1.2 ms, stays high, then releases at 14.0–14.2 ms.
Both common contacts change between separate receive-path and polarization-path test levels.
The contact outputs briefly fall near 0 V while both modeled paths are open.
Notes: LTspice 17.2.4 batch simulation completed on a relay-only test harness adapted from the four DPDT voltage-controlled contact models in complete_system.cir. Command timing follows that netlist: rises between 1.0 and 1.2 ms, remains energized through 14 ms, and releases by 14.2 ms. Distinct DC test levels (1 V/2 V on the NC receive side, 5 V/4 V on the NO polarization side) make each common contact’s selected path visible; these are test levels, not a coil-power or sensor waveform. Measured common-contact ranges: Lead A ~0.0006–5.001 V; Lead B ~0.0006–4.001 V. The brief near-zero output indicates the model’s all-open dead-band. This simulation does not test a physical relay coil, MOSFET driver, operate/release time, bounce, or load switching. Source: .presentation_build/relay_only.cir and local LTSpice/complete_system/complete_system.cir relay model.

## Slide 6
Feedback
06
Scan to share feedback
docs.google.com/forms · Proton Magnetometer project
Notes: Feedback form: https://docs.google.com/forms/d/e/1FAIpQLSfLOQv-7GeXDnTnMLijqTxS2kNHzPZWU2C_4p9spcn_NzkV5w/viewform